## Slide 1
MRC SRv6 Fabric
Computing uSID Carriers by Formula
How every GPU reaches every GPU — without storing an all-to-all table.
Reachability, multipath spray, and maintenance drain, all from one closed-form rule.
● spine ● leaf ● GPU SRv6 uSID (NEXT-C-SID / F3216) source routing

## Slide 2
THE PROBLEM
An all-to-all carrier table doesn't scale
The fabric could store one uSID carrier per source×destination×plane×spine.
That set grows quadratically with the GPU count:
carriers ≈ GPUs² · planes · spines
GPUs
carrier records
config size
128
409,088
237 MB
1,000
63 million
~38 GB
10,000
12.9 billion
~7.8 TB
Verified on real builds: 2× GPUs → ~4× bytes, 2× spines → ~2× bytes. Every byte is the enumerated mesh — the switch configs stay a few MB.
→ A production NIC must not hold this. The way out: don't store it — compute it.
MRC SRv6 Fabric · Carriers by Formula
2

## Slide 3
THE INSIGHT
Every address is position-encoded
Nothing about a carrier is arbitrary. Each field is a role, a plane, or an index —
so the 128-bit carrier to any destination is DERIVABLE from a few integers.
STORE (old)
one JSON record per
(src, dst, plane, spine)
→ O(GPUs²·planes·spines)
→ terabytes on disk
→ NIC holds a giant table
COMPUTE (new)
one formula + the fabric shape
(leaves, spines, planes, K)
→ O(1) on disk (~700 bytes)
→ NIC derives any carrier on demand
→ a couple of bit-shifts per path
The position-encoded uSID scheme was designed for exactly this.
MRC SRv6 Fabric · Carriers by Formula
3

## Slide 4
ANATOMY
What the bits mean
Two building blocks encode the whole fabric:
Switch locator — RPII hextet
RPII = role · 0x1000 + plane · 0x100 + index
role: spine = 1, leaf = 2 e.g. spine 1 in plane 1 → 0x1101
GPU decap uSID — 9LLL : GGGG
9LLL = 0x9000 + home-leaf index GGGG = GPU's local index on that leaf
gpu on leaf 2, local slot 2 → 9002 : 0002
Read any address and you can decode role, plane, and index straight out of it — and vice-versa, build the address from those numbers.
MRC SRv6 Fabric · Carriers by Formula
4

## Slide 5
THE FORMULA
One rule builds the carrier
carrier = block : <spine RPII> : e000+leaf : 9LLL : GGGG : 0 : 0
block = fcbb:bb00 (32-bit) · e000+leaf = spine's End.X toward the dst leaf
Worked example — gpu1 → gpu4, via spine 1, plane 1
fcbb:bb00
block (F3216)
1101
spine1 · plane1 (RPII)
e002
End.X → leaf 2
9002
GPU block + leaf 2
2
gpu4 local index
→ fcbb:bb00:1101:e002:9002:2::
The dst GPU's index and one chosen spine are all you need. The NIC assembles the 128-bit carrier with a few shifts — no lookup, no stored entry.
MRC SRv6 Fabric · Carriers by Formula
5

## Slide 6
REACHABILITY
Any GPU reaches any GPU
To reach a destination, the source computes the carrier and hands the packet to the fabric. The core does plain IPv6 longest-prefix forwarding — it stays dumb.
spine1
spine2
leaf1
leaf2
gpu1
gpu2
gpu3
gpu4
gpu1 → gpu4 carrier fcbb:bb00:1101:e002:9002:2::
computed,
not stored
MRC SRv6 Fabric · Carriers by Formula
6

## Slide 7
TWO PATH TYPES
Same-leaf and cross-leaf
SAME-LEAF
Peer on the same leaf — no spine hop.
The carrier names the destination's decap uSID directly; the leaf plain-forwards it.
block : 9LLL : GGGG ::
1 path per plane
e.g. gpu1 → gpu2
fcbb:bb00:9001:2::
CROSS-LEAF
Peer on another leaf — transits a spine.
The carrier names the spine's End.X plus the destination's decap uSID.
block : spine : e000+leaf : 9LLL:GGGG
one path PER SPINE, per plane → multipath
e.g. gpu1 → gpu4 via spine1
fcbb:bb00:1101:e002:9002:2::
MRC SRv6 Fabric · Carriers by Formula
7

## Slide 8
MULTIPATH
Planes × spines = the spray set
For a cross-leaf peer, the NIC generates one carrier per (plane, spine) — a set of physically-distinct paths it sprays traffic across for bandwidth and resilience.
EV 49007
plane1 · spine1
fcbb:bb00:1101:e002:9002:2::
EV 49008
plane1 · spine2
fcbb:bb00:1102:e002:9002:2::
EV 49009
plane2 · spine1
fcbb:bb00:1201:e002:9002:2::
EV 49010
plane2 · spine2
fcbb:bb00:1202:e002:9002:2::
All four EVs to the same GPU — only the spine RPII changes (1101 / 1102 / 1201 / 1202). Weighted spray + per-path health steer traffic onto the good ones.
MRC SRv6 Fabric · Carriers by Formula
8

## Slide 9
MAINTENANCE DRAIN
Draining a node or a plane
Drain is just set subtraction on the computed EVs. Mark a spine, leaf, or whole plane bypassed → every EV whose path touches it is flagged drained and loses its traffic share. It keeps being probed; nothing is deleted or rebuilt.
drain plane 2 → NIC reacts in ~2 s
EV 49007
plane1 · spine1
● active
EV 49008
plane1 · spine2
● active
EV 49009
plane2 · spine1
● DRAINED
EV 49010
plane2 · spine2
● DRAINED
what the NIC computes
drained_ids = {
direct-leaf1-p2,
spine1-p2,
spine2-p2
}
→ 5 / 10 paths drained
→ traffic re-sprays onto
the plane-1 EVs
The formula makes drain trivial: the plane/spine is simply excluded from the set the NIC (re)builds — verified live, reacts in ~2 seconds, restores just as fast.
MRC SRv6 Fabric · Carriers by Formula
9

## Slide 10
WHERE IT RUNS
Every NIC builds its own carriers
The generator emits a ~700-byte descriptor (block + shape + this GPU's index) instead of the enumerated table. The NIC expands it with the shared formula — in both modes.
STANDALONE
NIC reads the descriptor from its
profile file and calls mrc_usid.expand()
at load — programs per-EV seg6 encap.
descriptor → NIC → carriers
CONTROLLER (with GUI)
mrc-gui serves the SAME descriptor
over /api/mesh-plan; the NIC expands
its own carriers. Wire stays O(1).
gui → descriptor → NIC → carriers
One shared formula (mrc_usid.py) — verified byte-for-byte against the enumerated output, and validated live: 10/10 paths up, cross-leaf forwarding, drain all working.
MRC SRv6 Fabric · Carriers by Formula
10

## Slide 11
RESULTS
Terabytes → a formula
Enumerated table
Computed descriptor
10,000-GPU NIC state
~7.8 TB
a few MB
Per-GPU config
tens of MB
~700 bytes
Controller → NIC wire
O(paths)
O(1)
Reachability
every pair (stored)
every pair (computed)
Drain / planes / spines
works
works (set subtraction)
Switch configs are unchanged (a few MB at any scale). The quadratic was always the enumerated edge state — and now it's a rule the NIC evaluates on demand.
MRC SRv6 Fabric · Carriers by Formula
11

## Slide 12
TAKEAWAYS
One rule, the whole fabric
Position-encoded uSIDs
role·plane·index and 9LLL:GGGG make every carrier derivable.
Reachability for free
any GPU builds the carrier to any GPU; the core just LPM-forwards.
Multipath by construction
one EV per (plane, spine) — the spray set falls out of the formula.
Drain is set subtraction
exclude a spine/leaf/plane; the NIC re-sprays in ~2 s, nothing rebuilt.
O(1) everywhere
~700-byte descriptor on disk and on the wire; TB of table gone.
MRC SRv6 Fabric · Carriers by Formula
12